`

This document contains information and notes in hidden text.

If you need assistance to view & hide text, instructions are at this link:

http://www.marlite.com/hidden-notes-instructions.aspx

Delete this note and hyperlink after editing is complete.

The following specification has been developed by:

Marlite

202 Harger St.

Dover, Ohio 44622

Tel: (330) 343-6621 Fax: (330) 343-4668

Email:  info@marlite.com

Website: www.marlite.com

to assist Architects and Designers in the specification of Modules panel and trim that adhered to a smooth, solid, flat subwall. Module’s 15 standard square and rectangular panels are available in wood veneers as well as special Marlite Faux Prints applied to regular or no added formaldehyde backerboards engineered with tongue and groove joinery to form fine detailed grid patterns.

Refer to separate Marlite Guide Specification Sections 09 7710 sections for other Marlite Framed Decorative Panel and Trim systems, Sections 06 2500 and 06 4200 for Marlite prefinished panels, Section 09 7730 for Marlite decorative FRP panels,

The section has been formatted in accordance with the principals embodied in the Construction Specifications  Institute's  Manual of Practice and is intended for use in conjunction with Contract Conditions, Bidding Conditions and General Requirements developed in accordance with CSI guidelines.Notes to the specifier are included. Options that must be selected by the specifier are shown in brackets [         ].   Inapplicable clauses shall be deleted.

SECTION 09 7710 – ADHERED DECORATIVE PANEL SYSTEM

GENERAL

SUMMARY

Section Includes:   Decorative 1/4 inch (6.35mm) thick prefinished panel and trim for adhered installation on solid substrate.

Panels:

Wood Veneer on medium density fiberboard.

Marlite Faux Print (simulated wood grain) on medium density fiberboard.

Aluminum reveal and edge trim.

Aluminum base

Products Not Furnished or Installed under This Section:

Wood Veneer casework.

Gypsum Board backup.

Blocking for base.

RELATED SECTIONS

Section [____] - Wood [Metal] Stud Framing.

Section [____] - Custom Cabinets.

Section [____] - Solid Wood Paneling.

Section [____] - Gypsum Wallboard.

Section [____] - Painting & Transparent Finishes.

Section [____] - Resilient Base.

REFERENCES

References are listed as a convenience and are often deleted in their entirety.  If required by the user agency delete references from the list below that are not actually required by the text of the edited section.

American Society for Testing and Materials:  Standard Specifications (ASTM)

ASTM E 84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

Architectural Woodwork Standards as published by the Architectural Woodwork Institute, the Architectural Woodwork Manufacturers Association of Canada, and the Woodwork Institute.

Architectural Woodwork Standards - Edition 1.

SUBMITTALS

Product Data:  Submit sufficient manufacturer's data to indicate compliance with these specifications, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Shop Drawings:  Submit elevations of each wall showing location of paneling and trim members with respect to all discontinuities in the wall elevation.

Selection Samples:  Submit manufacturer’s standard [wood veneer] [print color and pattern] selection samples representing manufacturer's full range of available colors and patterns.

Samples for Verification:  Submit sample for each component and for each exposed finish required, prepared on samples of size indicated below complete with exposed molding and trim samples.  Sample to indicate type, finish, and color specified.

Prints:  Submit 6” (154mm) by 10” (254mm) section of panel for each panel selected indicating the color, texture, and pattern required.

Submit complete with specified applied finish.

For selected patterns show complete pattern repeat.

When matching custom veneer, request a flitch sample from the veneer to be used for the specific project after submission of a sample to be matched.

Wood Veneers:  Submit sample sets of [each] wood veneer with stain color and finish required.  Sample size approximately 6” (154mm) by 10” (254mm).  Sample sets to show the full range of normal color and texture variations expected.

Manufacturers Material Safety Data Sheets (MSDS) for panels, adhesives prior to their delivery to the site.

Maintenance Instructions

QUALITY ASSURANCE

ASTM E 84 Definition: Strict interpretation of the ASTM E 84 fire rating applies only to surface burning characteristics of a panel.  Architectural Panels comply with ASTM E 84 fire rating for a Class C material requires a flame spread of between 26 and 200, along with a smoke development maximum of 450.

ASTM E 84 fire rating for a Class A material requires a flame spread 25 or less, along with a smoke development maximum of 450.  Refer to Guide specification for Surface System MAP for Class A.

Conform to building code requirements for interior finish for smoke and flame spread requirements as tested in accordance with:

ASTM E 84 - Standard Test Method for Surface Burning Characteristics of Building Materials.

Required Rating – Class C.

DELIVERY, STORAGE AND HANDLING

Deliver panels packaged individually in plastic bags and plastic foam edge protectors.

Upon delivery open cartons and carefully inspect all panels for humidity damage.

Contact manufacturer if there are questions or problems.

Store products in manufacturer's unopened packaging until ready for installation.

Maintain plastic protection in place during on site handling until placing.

Do not stack panels after removal of protection.

Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of local authorities having jurisdiction.

PROJECT CONDITIONS

Composite panels are man made wood fiber products and are subject to the effects of humidity and temperature.  Do not use in kitchens, rest rooms, or other high humidity areas.

Partition walls are to be finished, and the building completely closed. Walls shall be thoroughly dry before starting installation.

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  To ensure product performance, a temperature range of 60°-80°F (16°C-27°C) and a humidity range of 35-55% must be maintained during storage, installation and product life cycle.  Do not install products under environmental conditions outside manufacturer's absolute limits.

COORDINATION AND SEQUENCING

Locate trim members so that panel lines are in line with doors headers jambs and other discontinuities in wall.

Vapor harrier shall be used on exterior walls behind backing to discourage warping.

Delete the following if panels are not used on casework.

Coordinate with casework manufacturer.  Deliver material to the fabrication shop.

WARRANTY

For longer warranties contact Marlite.

Standard Warranty:  All products shall be warranted to be free from defects for a period of 30 days after installation.

PRODUCTS

ACCEPTABLE PRODUCT

Marlite;   202 Harger Street, Dover, OH  44622.  800-377-1221 FAX (330) 343-4668 Email:  info@marlite.com www.marlite.com.

Product:  Modules Wall System.

PANELS

Select required face dimension.   Consult with Marlite before specifying custom size.

Panel face dimensions:  Nominal [48 inch (122cm) x 96 inch (244cm)]] [48 inch (122cm) x 48 inch (122cm)] [48 inch (122cm)  x 32 inch (81.28cm)] [48 inch (122cm) x 24 inch (61cm)] [48 inch (122cm) x 16 inch (41cm)] [24 inch (61cm) x 96 inch (244cm)] [24 inch (61cm) x 48 inch (122cm )] [24  inch (61cm)  x 32 inch (81.28cm)] [24 inch (61cm) x 24 inch (61cm)] [24 inch (61cm) x 16 inch (41cm)] [16 inch (41cm)  x 96 inch (244cm)] [16 inch (41cm) x 48 inch (122cm)] [16 inch (41cm)  x 32  inch (81.28cm)] [16 inch (41cm)  x 24 inch (61cm)] [16 inch (41cm) x 16 inch (41cm)]  [as indicated on the drawings].

Panel thickness  - 1/2 inch (12.7mm) thick,

Wood Fiber Substrate:

Medium density wood fiberboard conforming to ANSI A208.2, industrial-grade MDF or other wood fiber substrates having not less than 75% recycled wood waste

For panels that are to have minimum amount formaldehyde or higher recycled contents delete above and specify only Medium Density Fiberboard backer board with “No Added Formaldehyde”.

          - Medium density wood fiberboard conforming to ANSI A208.2, industrial-grade MDF and having No-Added Formaldehyde.

Wood Veneer Panels:   Selected wood veneer laminated to wood fiber substrate, and coated with furniture grade catalyzed finish.

Edges – Square cut and sealed.

Balancing Backer:   Wood veneer measuring between 0.015 inch (0.38mm) and 0.025 inch (0.64mm).

Veneer Face:  0.010 inch (0.25mm) to 0.015 inch (0.38mm) with a catalyzed finish of approximately 0.003 inch (0.08mm).

Grain direction is typically vertical but can be specified otherwise.

Grain direction and Veneer matching:  [Manufacturer’s standard] [As indicated on the drawings].

Refer to Marlite for veneer selections.  Panel cost can be significantly effected by veneer choice and must be should be stated below.

Species:  _________________________________________

Marlite Finish:  The base coats, precision and print coats and melamine top coats are applied to the most select substrate. Each panel is baked, creating a tough, durable finish that is easy to maintain.  The Marlite Finish is a richly detailed and easy to maintain surface that is more economical than decorative laminates. Wood grains, textures and abstract prints provide consistency in color and pattern.

Marlite Panel Finishes:  Modified melamine enamel (base coat, precision coats, print coats and melamine top coat) baked to achieve outstanding performance characteristics.

Select from the following Marlite standard finishes: Custom Capabilities - If you desire a different finish than our selection, simply submit your color/pattern sample and we’ll send you a lab sample match within a few days. Minimum production order quantities and lead times apply.  Actual product will vary. Please contact us for samples.

Faux Woodgrain:  [Marlite #038 Georgetown Anigr][Marlite #148 Monticello Anigre][Marlite #149 Montclair Anigre] [Sierra Maple Marlite #310][Alum Rock Maple Marlite #317][ Marlite #318 Windsor Anigre][Whittier Anigre Marlite #319] [Marlite #463-S4 Eastern Walnut] [Marlite #716-S4 Tropical Mahogany] [Marlite #715-S4 Mahogany] [Marlite #812-S4 Aged Cherry][Marlite #925-S4 Autumn Cherry][Marlite #938 Tuscany][Marlite #939 Verona] [Marlite #941 Laurel] [Marlite #943 Tulip] [Marlite #5401 Sebring][Marlite #5409 Townsend][Marlite #5411 Rainier] [Marlite #5414 Modena] [Marlite #5417 Solerno][Marlite #5420 Ceylon]

Color and Pattern:  _________________________________________ [As selected by Architect from manufacturer's standard selection.]

Edges – Eased and sealed, to provide a black edge.

HARDWARE

Panel Trim:  Aluminum Profiles  full 10’- 0” (3.05 meters) lengths

Panel Reveals – [1/8 inch Square] [1⁄4 inch Chamfered Reveal]

Edge/Inside Corner – Marlite #MT–570

Outside Corner – Marlite MT–560

Base Trim – Marlite #S-612.

Trim Material:   Heavy weight extruded aluminum 6063-T5 alloy and prefinished at the factory.

1.	Finish:  [Clear anodized.][Black satin anodized.]

ADHESIVES

Marlite Brand C109 adhesive is the adhesive recommended for installation of Modules.  Marlite Brand C-109 adhesive is a Low VOC solvent based material and local code restrictions may require substitution. Any adhesive substitution must have the manufacturer's approval.

Marlite Brand C-109 solvent based adhesive or as otherwise approved by Marlite.

FABRICATION

All framing, panels, hardware and accessories shall be factory finished and ready to install except for field fabrication as required by jobsite and perimeter conditions.

Refinish field cut panel edges in accordance with manufacturer’s instruction before installation.

For all cut-outs, drill corners for a minimum 1/8” radius.

EXECUTION

EXAMINATION

Installer's Examination:  Examine conditions under which construction activities of this section are to be performed.  Submit written notification to Architect and system manufacturer if such conditions are unacceptable.  Beginning erection constitutes installer's acceptance of conditions.

Verify that a vapor barrier has been provided on exterior walls behind backing to prevent warping.

Verify backing panels are smooth, solid, and flat.  [All drywall joints are to be taped and finished].

Verify that walls are to be primed before installation begins.

Verify mechanical, electrical, and building items affecting work of this section are placed and ready to receive this work.

Verify that stud spacing does not exceed 24” (600mm) on-center.

Structural walls are to be finished, with building completely closed.   Walls shall be thoroughly dry before starting installation.

PREPARATION

Conditioning:  Panels must be allowed to acclimate to a balanced environment in the installation location for 72 hours prior to installation.

Protect existing surfaces with drop cloths.

Due to textures, wood grain patterns, materials and manufacturing techniques, some panels may vary in color consistency, tone and pattern.  These variations are expected and not to be considered as defects. Contact Marlite with questions or problems.

Except as directed by the architectural drawings, before installing, examine panels and arrange to achieve best combination of color, pattern, texture and grain.

INSTALLATION

Install all materials in strict accordance with the manufacturer’s installation instructions with hardware straight, plumb, and level.

Anchor units rigidly and securely in place.

Cut sheets to meet existing supports.

Install edge and corner trim.  Cope intersections; do not allow trim flanges to overlap.  Secure trim with adhesives.   Avoid a heavy layer of adhesive to prevent squeeze-out.  Use 2 inch (50mm) strips of masking tape at 24” (600mm) on center for the length of the flange to hold until the adhesive cures.

Install panels on substrate using adhesive specified hereinbefore.

Dry-fit panels and make necessary cutouts.

Apply adhesive in a continuous bead around perimeter of hardware flange.

Apply a bead of adhesive approximately 6” (154mm) on center across panel width in accordance manufacturer’s recommended pattern.

Press and "knead" panels repeatedly to be certain of contact with the wall at all points. Fan the panel by pressing and pulling from the wall.

Avoid contamination of the panel faces with adhesives, solvents or cleaners during installation.

CLEANING AND PROTECTION

Clean and remove dust and other foreign matter from panel and framing surfaces.  Clean finishes in accordance with manufacturer's instructions.

END OF SECTION 09 7710