CSI Spec – Marlite Volta Panels

CSI Section - 09770

Part 1  General

  - Section Includes

- Marlite Volta Panels for decorative and retail use.

Use as perimeter wall, wall accent, floor fixture and retail display panels

.

  - Related Sections

- Section 06420 – Paneling: Architectural Paneling.

- Section 09771 – Decorative Wall Surfacing: Manufacured Paneling.

  - Submittals

- Product Data: Manufacturer’s product data sheets on each product to be used.

- Product Drawings: Manufacturer’s drawings showing details and dimensions.

- Product Installation: Manufacturer’s installation instructions and procedures.

- Product Samples: For each finish and pattern specified, select from manufacturer’s full rang of available colors and patterns.

  - Delivery, Storage And Handling

- Open packaging promptly after delivery and inspect panels carefully.

- Contact freight carrier if the product has been damaged in transit. Contact Marlite for any replacement order.

- Store product in a cool, dry environment.

- Do not subject panels to high humidity or moisture.

- Do not stack directly on the floor.

  - Project Conditions

- Condition panels to normal use temperature and humidity prior to installation.

  - Warranty

A.	All products shall be warranted to be free from defects for a period of 30 days after installation.

Part 2  Products

  - Manufacturer

A. 	Volta Panels shall be manufactured by: Marlite, 202 Harger Street, Dover, OH  44622.  ASD. Tel: 330-343-6621.  Fax: 330-343-7296.

E-mail: info@marlite.com

Website: www.marlite.com

09770-1

Part 2  Products (continued)

  - Materials

- All unfinished and pre-finished panels shall be Marlite Volta panels.

- Marlite Volta panels shall have a CNC created dimensional surface with panels typically matched at long edges to created a continuous appearance upon installation.  Specifier to choose from Marlite Finish Guide.

- Marlite Volta panels shall be constructed of the following.  Specifier to choose from Marlite Finish Guide.

    - High quality, 48# (+) density medium density fiberboard (MDF) substrate.  All MDF used for Volta panels shall comply to CARB Regulations, having formaldehyde emissions of .3 PPM or less and shall comply with HUD 24, CFR Part 3280 Standards as set for particleboards.

    - Resin impregnated, color thru wheat fiber board.

    - Resin impregnated, color thru sunflower seed fiber board.

    - Lightweight, composite, thermoplastic, fire-retardant, post-formed architectural panels.

- Marlite Volta panels shall have surface finish as follows.  Specifier to choose from Marlite Finish Guide.

    - Paint grade MDF for customer applied, on-site finishing.

    - MDF powdercoat (color per spec.).

    - Marlite Finish, low VOC, high solids, spray applied coating (color per spec.).

    - Vacuum laminated, thermo-formed and bonded architectural film (color/pattern per spec.).

2.3	Accessories

A.	Marlite Volta panels can be installed and trimmed out with a variety of  contractor supplied or Marlite hardware.  Specifier to choose from Marlite’s Finish Guide.

Part 3  Execution

  - Preparation

A.	All walls or partitions which are to receive Marlite Volta panels are to be solid, flat and dry.  Recommended stud spacing not to exceed 24” on-center.

09770-2

Part 3  Execution (continued)

B.	Marlite Volta panels may be installed directly over open studs, although a sub-wall covering of minimum ½” drywall or wood fiber board is recommended.

C.	Care should be taken to prevent moisture from penetrating through walls by supplying a proper vapor barrier.

D.	Refer to manufacturer’s installation instructions for wall board or vapor barriers.

3.2	Installation

A.	All Marlite Volta panels are to be installed in strict accordance with the manufacturer’s written installation instructions.

B.	Question regarding variances from recommended installation instructions should be referred to Marlite.

09770-3