Note:

This document contains information and notes in hidden text.

If you need assistance to view & hide text, instructions are at this link:

http://www.marlite.com/hidden-notes-instructions.aspx

Delete this note and hyperlink after editing is complete.

The following specification has been developed by

Marlite

202 Harger St.

Dover, Ohio 44622

Tel: (330) 343-6621 Fax: (330) 343-4668.

Email:  info@marlite.com  www.marlite.com

to assist Architects and Designers in the specification of Decorative Fiberglass Reinforced Plastic wall panel system for high wear areas.

Marlite Stamdard FRP Panels are excellent for sanitary environments since they facilitate washing and cleaning and do not support mold or mildew growth.  However, FRP panels are subject to the effects of continuous humidity and temperature.  Provide adequate ventilation for drying and do not use in high temperature areas.

Marlite Induro FRP provides an exceptionally wear resistant decorative panel; due to an exclusive process of thermally bonding melamine impregnated surfacing materials directly to the FRP core.  Designed to match or coordinate with popular High Pressure Laminates, these panels offer a superb array of decorative finishes and patterns from solid colors to wood-grains and abstract patterns.  Custom color and patterns are available upon request.

Marlite Artizan FRP panels offer a superb array of decorative printed rotogravure finishes with exceptional image integrity; unlimited varieties of woodgrain and abstract pattern plus tactile as well as visual textures.  Custom color and patterns are available upon request.

Marlite Envue Graphic FRP provides impressive visuals of high-resolution photographs, illustrations, logos, tile designs and custom graphics, all protected by Marlite’s tough Sani-Coat sealer. A special application process produces optimum graphic reproduction on a tough, sanitary surface.

Marlite Symmetrix with Sani-Coat FRP panels feature prefinished precision grid score lines that provide the look of tile without grout to clean or deteriorate.  Custom color and patterns are available upon request.

The section has been formatted in accordance with the principals embodied in the Construction Specifications  Institute's  Manual of Practice and is intended for use in conjunction with Contract Conditions, Bidding Conditions and General Requirements developed in accordance with CSI guidelines.

Notes to the specifier are included. Options that must be selected by the specifier are shown in brackets [         ].   Inapplicable clauses shall be deleted.

SECTION 09 78 13 – METAL INTERIOR WALL PANELS

GENERAL

SUMMARY

Section Includes:   Porcelain enameled steel faced panel with high density fiberboard (HDF) core and aluminum backer.

[Aluminum] trim.

Products Not Furnished or Installed under This Section:

Gypsum [Cementitious] substrate board.

Resilient Base.

RELATED SECTIONS

Section [____] – 	Gypsum [Cementitious] substrate board.

Section [____] - Wood [Metal] Stud Framing

Section [____] - Resilient Base.

REFERENCES

References are listed as a convenience and are often deleted in their entirety.  If required by the user agency delete references from the list below that are not actually required by the text of the edited section.

American Society for Testing and Materials:  Standard Specifications (ASTM)

ASTM D 3363 – Hardness

ASTM C 501 – Wear Resistance

ASTM D 2244 – Color Tolerance

ASTM D 2244 – Reflectance

ISO 15695 – Scratch Resistance

ISO 28722 – Graffiti Resistance

ISO 4532 – Impact Resistance

ISO 4892 – UV Resistance

ISO 28706-1 – Cold Acid Resistance

ISO 28706-2 – Boiling Acid Resistance

ASTM D523 – Orange Peel (Specular Gloss)

ASTM E84 – Standard Test Method for Surface Burning Characteristics of Building Materials

SUBMITTALS

Product Data:  Submit sufficient manufacturer's data to indicate compliance with these specifications, including:

Product Brochure

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Shop Drawings:  Submit elevations of each wall showing location of paneling and trim members with respect to all discontinuities in the wall elevation.

Selection Samples:  Submit manufacturer’s standard color pattern selection samples representing manufacturer's full range of available colors and patterns.

Samples for Verification:   Submit appropriate section of panel for each finish selected indicating the color, texture, and pattern required.

Submit complete with specified applied finish.

For selected patterns show complete pattern repeat.

Exposed Molding and Trim:  Provide samples of each type, finish, and color.

Manufacturers Material Safety Data Sheets (MSDS) for adhesives, sealants and other pertinent materials prior to their delivery to the site (available as downloads for most Marlite’s products at http://www.marlite.com/tech-details.aspx or by contacting Marlite at info@marlite.com).

QUALITY ASSURANCE

Conform to building code requirements for interior finish for smoke and flame spread requirements as tested in accordance with:

ASTM E 84 (Method of test for surface burning characteristics of building Materials)

Wall Required Rating – Class [A].Include the following if products are used in areas subject to stringent wash down requirements.

DELIVERY, STORAGE AND HANDLING

Deliver materials factory packaged on strong pallets.

Store panels and trim lying flat, under cover and protected from the elements.  Allow panels to acclimate to room temperature (range of 60 to 75°F) for 48 hours prior to installation.

PROJECT CONDITIONS

Environmental Limitations:  Building is to be fully enclosed prior to installation with sufficient heat (70°) and ventilation consistent with good working conditions for finish work

During installation and for not less than 48 hours before, maintain an ambient temperature and relative humidity within limits required by type of adhesive used and recommendation of adhesive manufacturer.

Provide ventilation to disperse fumes during application of adhesive as recommended by the adhesive manufacturer.

WARRANTY

Furnish one year guarantee against defects in material and workmanship.

PRODUCTS

ACCEPTABLE MANUFACTURER

Marlite;   1 Marlite Drive, Dover, OH  44622.  800-377-1221 FAX (330) 343-4668 Email:  info@marlite.com www.marlite.com.

Product:

a3™ CeramicSteel Architectural Panels

PANELS

a3 CeramicSteel surface, High Density Fiberboard (HDF) core, Aluminum backer.

Finish:  Standard Matte (approx. 30% Gloss), Standard Gloss (approx. 95% Gloss).

Dimensions:

Thickness – .250”

Width - 4'-0”  (1.22m) nominal, 47¾” actual

Induro FRP Panels are not available in lengths exceeding 8’ (2.4m).

Length – [10’-0” (3.0m) nominal, 119 ¾” actual][8’-0” (2.4m) nominal, 95¾” actual][As indicated on the drawings]

Tolerance:

Length and Width:  +/-1/8 “ (3.175mm)

Square -  Not to exceed 1/8 “ for 8 foot (2.4m) panels or 5/32 “ (3.96mm) for 10 foot (2.4m) panels

Properties:  Resistant to chemicals, scratch, bacteria, fire, graffiti and stain.

ASTM D 3363 – Hardness, greater than 9H.

ASTM C 501 – Wear Resistance, 0.1 g maximum.

ASTM D 2244 – Color Tolerance, comply with ASTM D 2244.

ASTM D 2244 – Reflectance, Y-value up to 93%.

ISO 15695 – 7 N minimum.

ISO 28722 – Graffiti Resistance, no color or gloss changes after cleaning.

ISO 4532 – Impact Resistance, no damage over 2mm after 24 hours (20 N load).

ISO 4892 – UV Resistance, comply with ISO 4892.

ISO 28706-1 – Cold Acid Resistance, Class A minimum.

ISO 28706-2 – Boiling Acid Resistance, 18.5 g/m2 maximum.

ASTM D523 – Orange Peel (Specular Gloss), comply with ASTM D523.

ASTM E84 – Standard Test Method for Surface Burning Characteristics of Building Materials, Flame spread 0, Smoke Developed 75, Class A rating.

Back Surface:  Smooth Aluminum backer.  Imperfections which do not affect functional properties are not cause for rejection.

Select finish from our full Marlite Finish Palette at www.marlite.com or contact Marlite to create your own finish.

Front Finish: [As Indicated on the Drawings] [In accordance with pre-approved sample.  Information available from the Architect’s Office][ __________________________________}

Specifier Note: Marlite a3 CeramicSteel Architectural Panels are available in Class A (I) fire-rating, along with various surface finish and color.

        - Color: [Specifier to choose.]

Marlite a3 CeramicSteel Architectural Panels are available in a variety of colors, including;

N-52 New White (Standard Gloss Finish)

PEI-14 Ivory (Standard Gloss Finish) *

PEI-22 Powder Grey (Standard Gloss Finish) *

513 Stone Grey (Standard Gloss Finish) *

PEI-29 Light Blue (Standard Gloss Finish) *

N-50 Medium Bronze (Standard Gloss Finish) *

1369 Bronze (Standard Gloss Finish) *

PEI-28 Glossy Black (Standard Gloss Finish) *

7563 Bone White (Standard Matte Finish) *

PEI-118 Stone White (Standard Matte Finish) *

5727 Colonial White (Standard Matte Finish) *

7477 Cream White (Standard Matte Finish) *

TCM-37 Sahara Sand (Standard Matte Finish) *

7568 Pueblo Tan (Standard Matte Finish) *

7571 Beige (Standard Matte Finish) *

N-125 Light Grey (Standard Matte Finish) *

7567 Fashion Grey (Standard Matte Finish) *

7569 Military Blue(Standard Matte Finish)  *

TCM-27 Red Clay (Standard Matte Finish) *

7570 Antique Bronze (Standard Matte Finish) *

7551 Hartford Green (Standard Matte Finish) *

TCM-60 Dark Bronze (Standard Matte Finish) *

TCM-14 Matte Black (Standard Matte Finish) *

3020 Traffic Red (Premium Color) *

5015 Sky Blue (Premium Color) *

5010 Gentian Blue (Premium Color) *

* minimum quantities may apply.

Custom imaging and colors are available.  Minimum quantities may apply.  Contact a Marlite representative for details.

        - Surface [Specifier to choose.] Standard Matte (approx. 30% Gloss), Standard Gloss (approx. 95% Gloss).

        - Fire Rating [Specifier to choose.] a3 CeramicSteel panels are available in Class A Fire Rating.

        - Size: [Specifier to choose, or as indicated on drawings.] standard sizes are;

          - a3 CeramicSteel panels

            - 4’ x 8’ x ¼” nominal, 47¾” x 95¾” x .250” actual.

            - 4’ x 10’ x ¼” nominal, 47¾” x 119¾” x .250” actual.

MOLDINGS

Select PVC or Aluminum trims.

Aluminum Trim:  Heavy weight extruded aluminum 6063-T5 alloy prefinished at the factory.

Profiles	:

The following are extruded aluminum trim profiles.

FC566 Ribbed Division Designer Trim, 8’ length

FC567 Radius Division Designer Trim, 8’ length

FC568 Square Channel Division Designer Trim, 8’ length

565 Division Trim, 8’ length

551 Inside Corner, 8’ length

560 Outside Corner, 8’ length

570 Edge, 8’ length

The following are extruded aluminum trim profiles.

Color:  [Factory Oven-Baked Harmonizing Finish to match spec’d panel][Black Satin Anodized][Clear Satin Anodized]

The following are extruded PVC trim profiles. PVC colors are also available to coordinate with Sani-Coat colorways.  See current Marlite Finish Guide for available choice.

Outside Corner Guard:

F 560SS Stainless Corner Guard, [8’ length][10’ length]

Finish:  #4 brushed satin

M 961 PVC Outside Corner Guard

Color: [White, [8’ length][10’ length]][Natural Almond, [8’ length][10’ length]][Ivory, 10’ length][Silver, 10’ length][Light Grey, 10’ length]

ACCESSORIES

Specify rivets for use in areas with dramatic changes in temperature and/or humidity, where the substrate is unusually uneven, and in all low temperatures or cold storage applications.

Adhesive:  Either of the following construction adhesives complying with ASTM C 557.

Marlite C-551 FRP Adhesive - Water- resistant, non-flammable adhesive.

Marlite C-915 Construction Adhesive - Flexible, water-resistant, solvent based adhesive, formulated for fast, easy application.

Sealant:

Marlite Brand MS-250 Clear Silicone Sealant.

Marlite Brand MS-251 White Silicone Sealant.

Marlite Brand - Color Match Sealant.

EXECUTION

PREPARATION

Examine backup surfaces to determine that corners are plumb and straight, surfaces are smooth, uniform, clean and free from foreign matter, nails countersunk, joints and cracks filled flush and smooth with the adjoining surface.

Verify that stud spacing does not exceed 24” (61cm) on-center.

Verify that sub wall has a vapor barrier to prevent moisture.

Repair defects prior to installation.

Level wall surfaces to panel manufacturer’s requirements.  Remove protrusions and fill indentations.

INSTALLATION

Comply with manufacturer's recommended procedures and installation sequence.

Cut sheets to meet supports allowing 1/8” (3 mm) clearance for every 8 foot (2.4m) of panel.

Cut panels “face-up” with a carbide-tipped table saw or cut panels “face-down” using a circular saw with a carbide-tipped blade. Leave protective film on panels when cutting.

Apply panels to board substrate, above base, vertically oriented.

Install panels with manufacturer's recommended gap for panel field and corner joints.

Adhesive trowel and application method to conform to adhesive manufacturer’s recommendations.

Apply panel moldings to all panel edges with required clearances.

All moldings must provide for a minimum 1/8” (3mm) of panel expansion at joints and edges, to insure proper installation.

Apply sealant to all molding channels for moisture-proof installations.

CLEANING

Remove excess sealant from panels and moldings.  Wipe panel down using a damp cloth and mild soap solution or cleaner.

Refer to manufacturer's specific cleaning recommendations.

END OF SECTION 09 7720